## Slide 1: Introduction to BIM Module 02 – Building Envelope

## Slide 2: Lesson Overview
In this lesson, students explore basics techniques for using the Autodesk® Revit® Architecture software to create a building information model of a simple structure—a one-story residence
Students will learn how to:
  Model wall types and design features.
  Create new wall types and edit their structure
  Place and adjust the properties of doors, windows, and wall openings
  Create roofs with different shapes and slopes

## Slide 3: Learning Objectives
After completing this lesson, students will be able to:
  Understand the methods for changing wall types and for creating new wall types with specific structures and design features
  Appreciate the techniques of placing doors and windows both in regular patterns and with appropriate height properties
  Explore methods for creating simple and complex roof elements modeling a variety of roof shapes and forms

## Slide 4: Essential Elements
Exterior Walls
  Windows
  Doors
  Openings
Roofs
  Openings
Curtain Walls
Columns

## Slide 5: Essential Elements
Aesthetic
  Mass vs. skeletal
  Materials >> Sustainability
Functional
  Support Loads
  Separate Exterior / Interior
    Thermal
    Lighting / Shading
Process
  Construction Technique

## Slide 6: Exercise 01: Modeling Wall Types and Features
In this exercise, students will be able to:
  Edit wall constraints and instance properties
  Define wall structure and adjust the material wrapping settings
  Add design features, such as sweeps and reveals
  Use stacked wall types
  Edit wall boundaries to create custom shapes

## Slide 7: Working with Walls
  Setting Instance Properties for Specific Walls
  Location Line
  Base
    Base Constraint
    Base Offset
  Top
    Top Constraint
    Top Offset

## Slide 8: Working with Walls
  Setting Type Properties for Basic Wall Types
  Structure
    Layers
    Function
    Materials
    Thickness >> Total
  Wrapping
  Vertical Structure
    Sweeps
    Reveals
    Regions & Layers

## Slide 9: Working with Walls
  Setting Type Properties for Stacked Types
  Structure
    Wall Type
    Height
    Offset
    Choose which Wall Type will have variable height

## Slide 10: Working with Walls
  Customizing Wall Boundaries
  Attach or Detach wall top and bottom
  Edit Wall Profile
    Create a custom top profile
    Pick another shape to follow
    Cut a custom opening

## Slide 11: Exercise 01: Modeling Wall Types and Features
  Student Exercise
Select and change the exterior walls to Exterior Brick
Create a new wall Type called Wood Panel Wall and specify the structure
Change all interior walls and exterior living room walls to type Wood Panel Wall
Attach the interior walls to the roof

## Slide 12: Exercise 02: Adding Doors and Windows
In this exercise, students will be able to:
  Place windows and doors and change their location using temporary dimensions
  Use arrays to place groups of regularly-spaced windows
  Edit door and window instance properties
  Create new window and door types
  Create wall openings

## Slide 13: Working with Windows
  Choosing Where to Place Windows
  Views
  Aesthetic effects
  Ventilation
  Lighting
  Solar Radiation
  Emergency Egress

## Slide 14: Working with Windows
  Adding Windows to Your Building Model
  Hosted by walls
  Working with Constraints
    Temporary Dimensions
    Equal Constraint
  Placing Groups
    Grouping elements
    Arraying groups

## Slide 15: Working with Windows
  Creating linear arrays of objects using Move To 2nd versus Move To Last
  Select an element to array
  Open the Array tool
  Use the Move To 2nd option to place all instances using the offset specified
  Using the Move To Last option to place all instances by dividing the distance specified equally

## Slide 16: Working with Windows
  Using the Group and Associate option with linear arrays
  Choose the Group and Associate option to create an array of associated elements
  Changes to any element in the array affect all other elements
    Number of instances
    Array length
    Changes to the group definition

## Slide 17: Working with Windows
  Setting Window Properties
  Instance Properties
    Level
    Sill Height
    Base Height
    Mark
  Type Properties
    Dimensions
    Trim
    Materials
    Inset

## Slide 18: Working with Windows
  Creating New Window Types
  Creating New Sizes
    Select similar window
    Duplicate an existing type
    Rename it
    Adjust size parameters
  Loading New Types
    From libraries
    Local
    Web

## Slide 19: Working with Windows
  Adding Wall Openings
  Load opening elements from library
    Use Component tool
    Load Family from Door section of library
    Place on wall
  Adjust size parameters
    Wall Opening tool
    Simple rectangular openings only

## Slide 20: Working with Doors
  Choosing Where to Place Doors
  Access / Circulation
  Emergency Egress
  Aesthetic effects
  Ventilation
    Desirable
    Undesirable
  If glazed, then
    Lighting
    Solar Radiation

## Slide 21: Working with Doors
  Adding Doors to Your Building Model
  Hosted by walls
  Working with Constraints
    Temporary Dimensions
    Equal Constraint
  Placing Groups
    Grouping elements
    Arraying groups

## Slide 22: Working with Doors
  Creating New Door Types
  Creating New Sizes
    Select similar door
    Duplicate an existing type
    Rename it
    Adjust size parameters
  Loading New Types
    From libraries
    Local
    Web

## Slide 23: Exercise 02: Adding Doors and Windows
  Student Exercise
  Place a Double-Glass type door at one end of the east living room wall, and then array it to create three instances
  Create similar arrays of Casement Dbl type windows in the dining and bedroom areas

## Slide 24: Exercise 03: Creating Roof Shapes
In this exercise, students will be able to:
  Create roofs by specifying their footprint and adjusting their properties
  Modify a roof footprint and slope-defining edges to fine-tune the create various roof shapes and forms
  Create a custom roof form by extruding a roof surface from a sketched profile

## Slide 25: Working with Roofs
  Defining Roofs by Footprint
  Sketch or pick walls to define the footprint
    Specify for each footprint line
    Defines slope?
    Overhang
    Extend to wall core?
  Set Base Level or Base Offset
  Choose roof type
  Attach walls to roof?

## Slide 26: Working with Roofs
  Choosing Slope Defining Edges
  Hip roofs
  Gable roofs
  Shed roofs
  Clerestory roofs
  Butterfly roofs

## Slide 27: Working with Roofs
  Defining Roofs by Extrusion
  Create reference plane (for extrusion profile) and name it
  Open Roof by Extrusion tool and choose work plane
  Draw single edge of extrusion profile
  Choose roof type
  Adjust start and stop of extruded roof shape

## Slide 28: Working with Roofs
  Creating New Roof Types
  Duplicate an existing type
    Select similar roof
    Duplicate an existing type
    Rename it
    Adjust structure
  Copy an existing type
    Defined within projects
    Transfer project standards
    Cannot copy from library

## Slide 29: Working with Roofs
  Specifying the Roof Edge Condition
  Overhang
  Rafter Cut
    Plumb Cut
    Two Cut – Plumb
    Two Cut – Square
  Fascia Depth
  Rafter or Truss
  Align eaves as needed for continuous roof edges

## Slide 30: Working with Roofs
  Joining Roof Elements
  Attach wall to roof
  Join roof edge to roof face
  Join roof edge to wall

## Slide 31: Working with Roofs
  Adding Roof Edge & Eave Details
  Fascia boards & gutters
    Choose profile
    Set offsets
    Pick edges
  Soffits
    Sketch boundary (in reflected ceiling plan view)
    Set elevation

## Slide 32: Exercise 03: Creating Roof Shapes
  Student Exercise
  Create a new roof by footprint over the triangular main living area of the project model
  Create another roof by footprint over the southeast bedroom wing
  Join the non-sloping edge of this bedroom area roof to the closest face of the living area roof to create a single roof

## Slide 33: Assessment
Modeling Wall Types, Structures, and Design Features
  How is the total thickness of a wall type computed?
  How can changing a wall’s type affect the clear space between adjacent walls?
  In a typical residence, what locations are most critically affected by the wall thickness?

## Slide 34: Assessment
Adding Doors, Windows, and Wall Openings
  Do the doors and windows move with the walls?
  Do doors and windows automatically adjust to the thickness of the host wall?
  What happens if the boundary of the door or window exceeds the extents of the wall?
  Can you place a door at a height above or below the associated floor level?

## Slide 35: Assessment
Creating Roof Shapes
  What would be the method for creating a barrel vault roof?
  How about a dome?
  A sloping roof surface surrounding a lower flat roof—a strategy often used to conceal utilities and mechanical equipment?
  What can you do if Revit reports that it cannot create a roof by footprint using the boundary sketched?

## Slide 36: Key Terms Used
Key Term | Definition
Stacked wall | A wall that has two or more horizontal layers, each consisting of different materials and surfaces.
Wall sweep | A horizontal or vertical projection from a wall, often decorative in nature. Examples of wall sweeps include baseboards and crown molding.
Revolve | Solid geometry that turns (revolves) around an axis. For example, you can use the Revolve tool to design a dome roof, a column, or door knobs.
Reveal | A decorative cutout in a wall.
Slope defining | Characteristic referring to of a roof edge’s role in defining the roof slope.